## Slide 1: KNN Classifier Accelerator
Backend Design Review
Students: Roy Rapaport, Dan Katz
Supervisor: Goel Samuel

## Slide 2: Outline
KNN Algorithm
Project’s requirements and specifications
Progress review: Stages covered
Top Level Architecture
Back-end stages
Milestones Ahead

## Slide 3: KNN Algorithm- Introduction
Definition: The K-nearest neighbors (KNN) is a non-parametric, supervised algorithm used for classification and regression tasks
Core Idea: KNN uses proximity to make classification or predictions about the grouping of an individual data point

## Slide 4: KNN Algorithm- Example
The example was taken from: https://towardsdatascience.com/

## Slide 5: KNN Algorithm- Example
The example was taken from: https://towardsdatascience.com/

## Slide 6: KNN Algorithm- Example
The example was taken from: https://towardsdatascience.com/

## Slide 7
Data representation: Requires labeled data points in a feature space
Distance Metric: Determine proximity using distance measures such as:
  Euclidean Distance -
  Manhattan Distance -
K selection: The parameter K specifies the number of nearest neighbors which needed for decision making
KNN Algorithm- How it works?

## Slide 8: KNN Algorithm- Steps
Data preparation: Store all training data in memory. In certain cases, we normalize or scale the training data to avoid biases from differing feature magnitudes
Compute distance: For each new test point, calculate the distance to all training points
Neighbor selection: Identify the K closest training points based on the chosen distance metric
Predict output:
  Classification: assign the class based on majority.
  Regression: assign the average value of the K-nearest neighbors

## Slide 9: Project’s Requirements and Specifications
KNN Algorithm:
  K: 5
  Number of groups: 2
  Distance Metric: Manhattan Distance
  Number of Train points: 128
  Data points range: [0,1023]

## Slide 10: Project’s Requirements and Specifications
Technology process: TSMC 65 nm
Maximum area: 1.0x1.0 sq mm
Maximum number of I/Os: 48
Clock frequency: 100 Mhz
Performance efficiency

## Slide 11: Progress Review: Stages Covered
Software Implementation
Architecture
RTL Implementation
Simulations
Synthesis with Scan Chain Insertion
Gate Level Simulation & LEC
Floorplan & Placement
Clock Tree Synthesis
Routing
Power Analysis & IR Drop
Timing Signoff
Physical Design Verification
Frontend
Backend

## Slide 12
29 Inputs pins, 10 Outputs pins
(+ 9 I/O for the Power Supply)
I/O Diagram
0 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 0 | 1
i_x Data Packet
X Value
Group

## Slide 13: Top Level Architecture
Smallest_5_distances_group_bit

## Slide 14: Top Level Architecture

## Slide 15: Top Level Architecture

## Slide 16: Backend design tools
Synthesis – Design Compiler (Synopsys)
Gate Level Simulation – VCS (Synopsys)
Logical Equivalence Check (LEC) – Conformal (Cadence)
Physical Design – Innovus (Cadence)
Timing Signoff – PrimeTime (Synopsys)
Physical Design Verification – Virtuoso (Cadence)

## Slide 17: Synthesis
Translating RTL code into a gate-level netlist using standard cell libraries.
Applies algorithms to minimize area and power while preserving the intended functionality.
Scan chains are inserted to improve testability.
Clock gating is inserted for power reduction.
In our KNN Classifier Accelerator:
  Ultra Compile
  2 Scan chains
  No Clock gating

## Slide 18: Logical Equivalence Checking -lec
Case 1:
  Used compile (no scan chains, no clock gating) : Netlist vs. RTL comparison using LEC: Passed
Case 2:
  Used ultra compile (no scan chains, no clock gating) :Netlist vs. RTL comparison using LEC: Passed
Case 3:
  Used ultra compile with 2 scan chains, no clock gating: Netlist vs. RTL comparison using LEC: Passed
Case 4:
  Used compile with 2 scan chains and clock gating: Netlist vs. RTL comparison using LEC: Failed.
✅ Selected Configuration: Case 3 : Validated with Gate-Level Simulation: Passed

## Slide 19: Logical Equivalence Checking -lec

## Slide 20: Gate level simulation
  RTL:
  Synthesis:
Gate Level Simulation – RTL Vs. Synthesis with scan chains + pads

## Slide 21: Physical design - floorplan
Die creation & chip size determination: Die size: Width: 890 [um] Height: 830 [um]
Power & I/O PADs positioning: Core to IO Boundary: 52 [um]
Power Ring & Grid Generation.
CLK
Core
VDD
Core
VSS
Core
VSS
Core VDD
I/Os VDD
I/Os VSS
I/Os VDD
I/Os VSS

## Slide 22: Physical design - placement
Standard cells placement, while optimizing:
  Timing
  Wire length
  Area
  Power
Maximum Density: 0.35

## Slide 23: Physical design – clock tree synthesis (cts)
Critical process that aims to minimize skew, insertion delay
The process ensure that the clock signal reaches all the FF in the design nearly at the same time
Delay : 220-280ps
Skew: 60ps

## Slide 24: Physical design – routing
This process employs metal layers to physically connect signal pins
Performs subsequent optimizations to connect standard cells, macros, and I/O pins
Creates electrical pathways with metals and vias based on the logical connections from the netlist

## Slide 25: Physical design – power analysis
Static Power Analysis result using innovus:
  FastRC Total Power Consumption: 42.95 [mW]
  SlowRC Total Power Consumption: 29.84 [mW]
Dynamic Power Analysis result using innovus:
  Dynamic peak power consumption was 0.1396 W — the peak usage in both FastRC and SlowRC scenarios.

## Slide 26: Physical design –rail analysis
IR Drop Analysis: Rail analysis checks voltage drops in the power grid to ensure they stay within safe limits, avoiding failures caused by low voltage.
IR Drop Limit: Must be below 7% of 1.2 V, i.e., should not exceed 84 mV.
  The VDD IR drop: 13.28mV
  The VSS IR drop: 12.87mV
For the IR Drop Analysis we used:
  Input activity: 0.2
  FF activity: 0.4
  Freq: 100 [MHz]

## Slide 27: Physical design –rail analysis
VDD:
VSS:

## Slide 28: Physical design – Timing SIGNOFF
Perform Static Timing Analysis (STA) before fabrication
Verifies that all data paths meet timing requirements at the target clock frequency
Accounts for on-chip variations that may affect signal delays
  Analyze both Setup and Hold timing constraints
  Use two temperature corners: –40°C and 125°C
  Include three library cell types with varying speeds (e.g., slow, typical, fast)
Critical path delay: 9.885ns

## Slide 29: Physical design – Add bond pads
Total size: Width:1060[um] Height: 1000 [um]

## Slide 30: Physical design – Physical Design Verification
Passed LVS and DRC

## Slide 31: Milestones Ahead
Preliminary GDS Submission (20.07.25)
Tapeout deadline (20.8.25)

## Slide 32
THANK YOU!